***** File IMSHERS.DOC                                                        
                                                                              
           EXPLANATION OF THE IMS/HERS DATA FORMATS                           
                                                                              
                                                                              
This document describes the format of the Giotto Ion Mass                     
Spectrometer/High Energy Range Spectrometer (IMS/HERS) data                   
submitted to the International Halley Watch Data Archive.  A                  
description of the experiment has been published in Balsiger et al.,          
ESA-SP 1077, pp 129-148, European Space Agency,     March, 1986               
(republished in J. Phys. E: Sci. Instrum., 20,  759, 1987.)                   
                                                                              
For proton and alpha-particle data, the ASCII files can be                    
read with the following FORTRAN statements:                                   
                                                                              
    OPEN(1,FILE='filename',STATUS='OLD',READONLY)                             
    READ(1,2)IDAY,IUT,DECHR,VX,VY,VZ,DEN,TLOG                                 
2   FORMAT(1X,I3,I8,F8.3,3F7.0,F7.1,F7.2,5X)!for protons                      
2   FORMAT(1X,I3,I8,F8.3,3F7.0,F7.2,F7.2,5X)!for "alphas"                     
                                                                              
On the tape as provided to the International Halley Watch, this               
file and three other files were supplied with 60 byte records                 
and a block size of 600 bytes.   The last data file (M/Q>12)                  
was subsequently broken into 10 pieces as listed in Appendix A.               
                                                                              
For heavier ions, the following FORTRAN statements should be used:            
                                                                              
        OPEN(1,FILE='filename',STATUS='OLD',READONLY)                         
        READ(1,2)IDAY,IUT,ISEC,DECHR,VX,VY,VZ,DEN,TLOG                        
2       FORMAT(1X,I3,I8,I6,F8.3,3F7.0,F6.1,F7.2)                              
                                                                              
Where the parameters have the following meanings:                             
IDAY = Day of year  (Day 72 = March 13, 1986)                                 
IUT = Spacecraft event time in hhmmss at the center of the                    
measurement interval                                                          
ISEC = Length of averaging interval in seconds (Heavy ions only)              
                                                                              
DECHR = IUT converted to decimal hours                                        
VX = x component of velocity, in km/s, in HSE coordinates                     
VY = y component of velocity, in km/s, in HSE coordinates                     
VZ = z component of velocity, in km/s, in HSE coordinates                     
DEN = density, in particles/cm**3                                             
TLOG = Log (base 10) of temperature (K)                                       
                                                                              
HSE coordinates are Halley-relative Solar Ecliptic                            
coordinates                                                                   
Vx is the velocity component toward the Sun                                   
Vz is the velocity component toward the north ecliptic pole                   
Vy forms a right-handed system                                                
The temperature is defined by 3nkT = m(v - <v>)**2                            
                                                                              
It must be emphasized that the IMS/HERS instrument could not                  
detect ions with spacecraft-relative velocity vectors within                  
15 degrees of the ram direction.  The method of data                          
reduction assumed spherical shell distributions, and                          
corrected for the portion of a spherical shell outside the                    
field of view of the experiment.  However, if a spherical                     
shell fell entirely within the blind area, no correction                      
could be made.  These unmeasured cold ions are an important or                
the major component of the ion density after ~2345UT, March 13.               
                                                                              
The following files are included in the data set.                             
PROTONS.IHW                                                                   
ALPHAS.IHW                                                                    
HEAVY.IHW                                                                     
                                                                              
For protons, the data start at 1830 UT on March 13 and                        
extend to the time of instrument failure at 0003 UT on                        
March 14.  For alphas, the data also start at 1830 UT on                      
March 13 but end at 2330 UT, March 13, after which it became                  
difficult to separate He++ ions from the H2+ (see Fuselier                    
et al., Geophysical Research Letters, Vol. 15, pages 549-                     
552,1988). For heavier ions, we give data only when the                       
fluxes were large enough to permit calculation of density                     
and temperature.                                                              
                                                                              
Until 2348 UT on March 13, proton spectra were obtained                       
every 4th spacecraft spin (i.e., one measurement every 16                     
seconds) and the data are given at this time resolution,                      
with some gaps corresponding to missing or erroneous data.                    
After 2348 UT, the data mode changed such that 8 spins                        
(32 s) were required to obtain a proton spectrum. The proton                  
parameters were calculated using a moment summing technique.                  
The estimated densities include corrections for protons                       
outside the field of view of the experiment; the corrections                  
were based on the assumption that the proton distribution                     
was isotropic.                                                                
                                                                              
Alpha spectra were also obtained every 4th spacecraft spin                    
and four consecutive spectra have been summed before                          
calculation of the physical parameters.  The time resolution                  
of the "alpha" data is therefore 64 s. The estimates of the                   
alpha parameters were obtained by fitting to an isotropic                     
distribution, and the estimated densities include                             
corrections for alphas outside the field of view of the                       
experiment.                                                                   
                                                                              
The heavier ion spectra are at nonconstant intervals because                  
it was possible to obtain estimates more frequently when                      
fluxes were higher. Data are given only for those intervals                   
and those species for which there were at least 8 counts in                   
the appropriate part of phase  space. Note that the                           
components of velocity are independent of M/Q for any given                   
interval. This results from the method of calculation.  For                   
each interval, the water-group ions (M/Q = 16-18) were used                   
to determine the velocity that gave the best (least-squares)                  
fit of the ion distributions to an isotropic distribution.                    
For each time interval, the best-fit water-group vector                       
velocity was then used to transform the measured velocity                     
distribution for each ion species into a moving coordinate                    
system in which the density and temperature were calculated,                  
again assuming isotropy. The estimated densities include                      
corrections for ions outside the field of view of the                         
experiment.                                                                   
                                                                              
To convert from time to cometocentric distance:                               
Distance (km) = (24.05 - dechr) * 3600 * 68.4                                 
                                                                              
For further information, contact one of the following                         
people at:                                                                    
                                                                              
Mail Stop 169-506,                                                            
                                                                              
Jet Propulsion Laboratory,                                                    
Pasadena, CA 91109,                                                           
USA:                                                                          
Bruce E. Goldstein, Telephone 818-354-7366                                    
Raymond Goldstein, 818-354-0241                                               
Marcia Neugebauer, 818-354-2005                                               
                                                                              
*******************************************************************           
                                                                              
                        Appendix A                                            
                                                                              
Note: a corrected file of "HEAVY" densities was sent on April 3, 1991.        
These data have been reformatted into separate files.   A complete list       
of files, including protons and alphas, follows:                              
                                                                              
Filename            Content                                                   
                                                                              
IMSHER01            protons                                                   
IMSHER02            alphas                                                    
IMSHER03            M/Q = 12                                                  
IMSHER04                  13                                                  
IMSHER05                  14                                                  
IMSHER06                  15                                                  
IMSHER07                  16                                                  
IMSHER08                  17                                                  
IMSHER09                  18                                                  
IMSHER10                  28                                                  
IMSHER11                  29                                                  
IMSHER12                  32                                                  
                                                                              
*******************************************************************