Galileo Magnetometer, Gaspra Browse Data - Additional Documentation
===================================================================

[These data were extracted from the separate catalog files originally
 provided with the BROWSE data file.]


      Dataset Overview
      ================

      This dataset contains data acquired by the Galileo Magnetometer
      during the Gaspra flyby on Oct 29, 1991. The browse dataset has
      been created by averaging samples from the  7.68 kB Low Rate
      Science (LRS) tape record mode to 20 second sampling and merging
      the data with the 8 RIM averages of the optimal averager to
      provide a continuous dataset for the encounter day. The
      magnetometer high time resolution recorded data include a few
      short intervals in the solar wind prior to the encounter, plus
      a main ~two hour recording near closest approach.  The optimal
      averager section of the instrument (please see the instrument
      description) was configured to acquired 8 RIM (~8 minute)
      averages to fill in the gaps between the recorded intervals. All
      of these data have been fully processed to remove instrument
      response function characteristics and interference from magnetic
      sources aboard the spacecraft. The magnetometer data are provided
      in heliographic (RTN) coordinates. Trajectory data have been
      provided as a separate archive product.

      Primary Dataset Reference:

        Kivelson, M. G., L. F. Bargatze,  K. K. Khurana, D. J. Southwood,
        R. J. Walker, P. J. Coleman, 'Magnetic Field Signatures Near
        Galileo's Closest Approach to Gaspra', Science, Vol. 261, p331-334,
        16 July, 1993.

      Primary Instrument Reference:

        Kivelson, M. G., K. K. Khurana, J. D. Means, C. T. Russell, and
        R. C. Snare, 'The Galileo magnetic field investigation', Space
        Science Reviews, 60, 1-4, 357, 1992.

          Data Columns:

       time    S/C event time (UT) given in PDS time format
                  YYYY-MM-DDThh:mm:ss.sssZ
       Br      Magnetic field radial component in RTN coordinates <nT>
       Bt      Magnetic field tangential component in RTN coordinates <nT>
       Bn      Magnetic field normal component in RTN coordinates <nT>
       Bt      Average magnetic field magnitude <nT>

       Missing data value = 99999.999
       Fortran Format of the data file: (1X, A24, 4F11.3)


      Data Acquisition:

      The data for this dataset were acquired by the outboard magnetometer
      (flip left position) in the low field (+/- 32 nT) mode (ULLR).
      has a digitization step size of 0.0625 nanoTesla. However, these
      data are acquired at 30 vectors/second and then recursively filtered
      in the instrument. The high rate data that are recorded to tape have
      a sample rate of 4.5 vectors/second. If there is sufficient variation
      in the 6-7 input samples that make up a single output sample, then
      the effective digitization step size becomes much smaller. The long
      averages provided in the browse dataset should not show any
      quantization effects.

      Data Sampling:

      The high rate recorded data are not evenly sampled within a minor
      frame. However, these data have been averaged using an averaging
      routine to produce evenly sampled data. The averaging process takes
      all available data during a 20 second period centered on the output
      time tag. Averages are not overlapping. The time tag gives the
      spacecraft event time (SCET) of the center of the averaging interval
      in universal time (UT).

      The optimal averager section of the instrument 'averages' data by
      applying a recursive filter to onboard processed and despun data
      and then decimating the data at the appropriate sample times. This
      process is explained in detail in the 'cruise' dataset that has
      been included with this archive product. The final processed
      product that has been incorporated into this dataset is sampled
      about every 8 minutes where the time tag marks the center of the
      averaging interval in SCET / UT.


      Coordinate System
      =================

      The data are provided in heliographic  RTN (radial-tangential-normal)
      coordinates. The radial direction is taken along the instantaneous
      Sun->S/C line, positive away from the sun. The tangential direction
      is found by taking the cross product of the sun spin axis with the
      radial (T = Omega x R) direction. Finally, the normal direction is
      the cross product of R and T (N = R x T).



    CONFIDENCE_LEVEL_NOTE

      The sources of error which are the most significant are those
      associated with magnetic sources aboard the spacecraft, especially
      those with temporal or spacecraft orientation variations. The next
      greatest contributor of error is the data from the AACS which
      affects our knowledge of the spacecraft orientation and hence
      rotates the magnetic field vector. Lastly, telemetry or software
      errors which produce 'spikes' or bit errors in the data are error
      sources.

      In this dataset the magnetic sources associated with the spacecraft
      were fairly constant and magnetic field values are accurate to at
      least 0.01 nT. The spacecraft orientation has been well determined
      and is known to better the 0.1 degree.