Galileo Magnetometer, Gaspra High-Resolution Data - Additional Documentation
============================================================================

[These data were extracted from the separate catalog files originally
 provided with the HRSC and HRGEOPH data files.]


      Dataset Overview
      ================

      This dataset contains data acquired by the Galileo Magnetometer
      from the Gaspra encounter. The data are at the full instrument
      resolution for the 7.68 kB Low Rate Science (LRS) real time
      telemetry mode. These data have been fully processed to remove
      instrument response function characteristics and interference
      from magnetic sources aboard the spacecraft. The data are provided
      in physical units (nanoTesla) in 4 coordinate systems. One of the
      data files contains data in Inertial Rotor Coordinates (IRC = despun
      spacecraft). This file includes many of the data processing
      parameters from the AACS system as well as the sensor zero levels.
      The other data file contains magnetic field data in Gaspra-centric
      Solar Ecliptic (GaSE), Earth Mean Equatorial equinox 1950 (EME-50),
      and finally in Heliographic (RTN) coordinates.

      Trajectory data are provided as a separate dataset for each of the
      geophysical coordinate systems.

      Primary Dataset  Reference:

        Kivelson, M. G., L. F. Bargatze,  K. K. Khurana, D. J. Southwood,
        R. J. Walker, P. J. Coleman, 'Magnetic Field Signatures Near
        Galileo's Closest Approach to Gaspra', Science, Vol. 261, p331-334,
        16 July, 1993.

      Primary Instrument Reference:

        Kivelson, M. G., K. K. Khurana, J. D. Means, C. T. Russell, and
        R. C. Snare, 'The Galileo magnetic field investigation', Space Science
        Reviews, 60, 1-4, 357, 1992.


      Data Acquisition:

      The data were acquired by the Galileo Magnetometer in the normal
      Low Rate Science (LRS) manner except that the data were recorded
      to tape and played back during the Earth 2 encounter. The data
      were acquired by the outboard magnetometer in the flip left
      position and the low range (high gain) mode.

      The Galileo magnetometer has 8 possible LRS acquisition
      configurations (modes). There are two sensor triads mounted
      7 and 11 meters from the rotor spin axis (inboard and outboard)
      along the boom. Each of the sensor triads has two gain states
      (high and low).  In addition, the sensor triads can be 'flipped'
      to move the spacecraft spin-axis aligned sensor into the spin
      plane and visa versa. Please see the instrument description for
      full details on the instrument, sensors, and geometries. The
      combinations of sensor, gain state, and flip direction form modes.

         _____________________________________________________________________
                                   Mode Characteristics
         _____________________________________________________________________
                  Mode Name            Acronym         range      quantization
         _____________________________________________________________________
         Inboard,  left,  high range*    ILHR      +/- 16384 nT       8.0   nT
         Inboard,  right, high range*    IRHR      +/- 16384 nT       8.0   nT
         Inboard,  left,  low  range*    ILLR      +/-   512 nT       0.25  nT
         Inboard,  right, low  range*    IRLR      +/-   512 nT       0.25  nT
         Outboard, left,  high range*    ULHR      +/-   512 nT       0.25  nT
         Outboard, right, high range*    URHR      +/-   512 nT       0.25  nT
         Outboard, left,  low  range*    ULLR      +/-    32 nT       0.008 nT
         Outboard, right, low  range*    URLR      +/-    32 nT       0.008 nT

          * range is the opposite of gain

      Data Sampling:

      The Galileo magnetometer samples the magnetic field 30 times
      per second. In order to reduce the data rate to the MAG LRS rate,
      the instrument performs an onboard averaging process.  The high
      rate samples are recursively filtered

          Recursive Filter

          B(t) = 1/4 Bs(t) + 3/4 B(t-1)

          B  = output field
          Bs = input field measured by the sensor
          t  = sample time

      and then resampled by the instrument at 4.5 vectors per second
      using a 7,7,6 decimation pattern. The pattern is generated by
      doubling the spacecraft clock modulo 10 counter and then applying
      the decimation scheme. This gives 3 vectors every spacecraft minor
      frame (about 2/3 second) which are sampled unevenly. The first
      vector in a minor frame is sampled approximately 0.200 seconds
      after the last vector in the preceding minor frame. The other two
      samples are taken approximately 0.233 seconds apart. The time tag
      associated with a sample is the decimation time.

      Coordinate Systems:

      The Galileo magnetometer data are being archived in 4 coordinate
      systems. The first coordinate system is referred to as inertial
      rotor coordinates (IRC). This coordinate system has the Z axis
      along the rotor spin axis, positive away from the antenna, and
      the X and Y axes lie in the rotor spin plane. In a crude sense,
      when the spacecraft is far from Earth, positive X points south,
      normal to the ecliptic plane, positive Y lies in the ecliptic
      plane in the sense of Jupiter's orbital motion and positive Z is in
      the anti-earth direction. The spacecraft antenna (negative Z
      direction) is kept earthward pointing to about +/- 10 deg accuracy.

      Gaspra-centric Solar Ecliptic (GaSE) is a Gaspra centered
      coordinate system defined by the primary vector along the
      instantaneous Gaspra->Sun (GSun) line and the Earth's ecliptic
      north pole (ENP) as the secondary vector. In this coordinate system:

         X is the GSun unit vector taken to be positive towards the sun.
         Y is the vector formed by the unitized cross product ENP x GSun
         Z completes the right-handed set (Z = X x Y)

      such that the X-Z plane contains the ecliptic north pole.

      The Earth Mean Equatorial equinox of 1950 (EME-50) coordinate system
      is an inertial reference system. The primary vector in this system
      points from the Earth towards Aries at the reference epoch. The
      secondary vector is along the Earth's rotational axis positive
      towards its north pole. In this coordinate system:

         X is a unit vector in the direction of Aries at the equinox of 1950
         Y is a unit vector in the direction of Z x X
         Z is a unit vector in the direction of the Earth's equatorial north
           pole at the equinox of 1950.

      The EME-50 coordinate system is directly supported by SPICE as the
      'FK4' inertial reference frame.

      The heliographic (RTN) coordinate system is centered at the sun. The
      primary vector in this system points from the center of the sun to the
      spacecraft (R). The secondary vector in this system is the sun's north
      rotational axis (Omega).

         R is along R, positive away from the sun.
         T is along the cross product Omega x R
         N completes the right-handed set (R x T)


      Data Processing:

      These data have been processed from the PDS dataset:
      'GO-E/V/A-MAG-2-RDR-RAWDATA-HIRES-V1.0'

      The 'raw data' product was created from the EDR dataset by removing
      the data processing done by the instrument in space. The raw data
      product contains the raw instrument samples which have been recursively
      filtered and decimated as described above. The processed data in IRC
      coordinates were rotated into geophysical coordinates using the SPICE
      libraries and kernels provided by NAIF.  In order to generate the IRC
      processed data, the following procedure was followed:

      1)  Sensor zero level corrections were subtracted from the raw data.
      2)  Data were converted to nanoTesla.
      3)  A coupling matrix which orthogonalizes the data and corrects for
            gains was applied to the data (calibration applied).
      4)  Magnetic sources associated with the spacecraft were subtracted
            from the data.
      5)  Data were 'despun' into inertial rotor coordinates.


      1) Zero level determination: The zero levels of the two spin plane
         sensors were determined by taking averages over a large number
         (about 50) of integral spin cycles. The zero level of the spin
         axis aligned sensor was determined by a variety of means. First,
         since the spin axis aligned sensor can be flipped into the spin
         plane, the value of the zero level determined in the spin plane
         can be used in the other geometry. This works well if there are
         no spacecraft fields and the zero level is stable. If there are
         spacecraft fields present which remain constant over relatively
         long time periods (many hours), then another method of zero level
         determination is used. The spacecraft spin axis is along the Z
         direction; the data in the X and Y directions have already had
         zero level corrections applied.

             Bm(z)   = B(z) + O(z)
             |Bm|^2  = B(x)^2 + B(y)^2 + Bm(z)^2
                     = B(x)^2 + B(y)^2 + B(z)^2 + O(z)^2 + 2B(z)O(z)
                     = |B|^2 + O(z)^2 + 2B(z)O(z)
                     = |B|^2 + O(z)^2 + 2O(z)[Bm(z)  - O(z)]
                     = |B|^2 - O(z)^2 + 2O(z)Bm(z)

            m = measured value    -    no subscript = true value

         Now if |B| remains constant over a short interval and O(z) remains
         constant over a much longer interval, we can take averages and
         reduce this equation to:

         |Bm|^2 - <|Bm|^2> =  2O(z)[Bm(z) - <Bm(z)>]

         <> indicates average value

         Data can be processed using short averages of |B| until many
         points are accumulated and then fit with a line in a least
         squares sense. The slope of this line is twice the required
         offset. The scatter in the data give an indication of the
         error in the assumption that |B| and O(z) have remained constant.
         Intervals with large rms errors are not retained. The zero levels
         removed from the data are given in the IRC data file.

      2) Conversion to nanoTesla simply requires dividing the instrument
         data numbers by a constant scale factor. For the inboard high
         range (low gain) mode the scale factor is 2. For the inboard low
         range and outboard high range, the scale factor is 64. The
         outboard low range data has a scale factor of 1024.

      3) Calibration matrix applied: The determination of a calibration
         matrix is too complex to describe here. The method employed has
         been well described in 'A Fourier Transform Based Method for
         Intraspacecraft Magnetometer Calibration', K.K. Khurana, E.L.
         Kepko, and M.G. Kivelson, (in press).

      4) After the data were initially processed (calibrated and despun),
         it was clear that there were still coherent noise sources remaining
         in the data. Dynamic spectra of the magnetometer data revealed
         coherent energy at high order (2nd, 3rd, 4th) harmonics of the spin
         period. High order harmonics of the spin period can be generated by
         spinning about a fixed dipole source such as a source on the despun
         platform. The source of the high order harmonics was modeled using
         1-D (spacecraft clock angle) Fourier transforms of high pass
         filtered data. This allowed us to resolve the source in terms of
         the relative spin phase of the scan platform. Model fields
         associated with this source (approximately 0.15 nT at the inboard
         sensors in the lowest harmonic) have been subtracted from the data.

      5) Despinning: Data are despun and checked in inertial rotor
         coordinates before transforming to geophysical coordinates. Any
         errors in the processing will be most readily apparent in inertial
         rotor coordinates. The  nominal transformation to IRC from SRC is

            (Bx)   ( cos(theta)   -sin(theta)  0 ) (Bxs)
            (By) = ( sin(theta)    cos(theta)  0 ) (Bys)
            (Bz)   (   0               0       1 ) (Bzs)

         Where s denotes spinning coordinates and theta is the rotor spin
         angle.

         Frequency dependent phase delays associated with the analog
         anti-aliasing filter and the digital recursive filter have been
         removed during the despinning of the data. The dominant frequency
         in the spinning data is at the spacecraft spin frequency. The phase
         angle delay associated from all known sources is computed at the spin
         frequency and removed from the data during despinning.

         Analog Filter:              Digital Filter (Nyquist Freq Fn = 15Hz)

               1543                         1/3
         __________________          _____________________
         s^2 + 55.5s + 1543           4/3 - exp(-PI*i*f/Fn)

         s = 2*PI*i*f

         Imaginary = 55.5s          Imaginary = -sin(PI*f/Fn)
         Real      = 1543 + s^2     Real      = 4/3 - cos(PI*f/FREQ_N)


         f = frequency
         delay = tan^-1(Im/Re)

         In addition, there is an electrical delay associated with the A/D
         conversion of about .037 milliseconds. This delay is converted to
         an angle using the instantaneous spin frequency. These 3 sources
         of delay are then summed in to the quantity 'phase' and then the
         despinning matrix becomes:


            (Bx)   ( cos(theta - phase)   -sin(theta - phase)  0 ) (Bxs)
            (By) = ( sin(theta - phase)    cos(theta - phase)  0 ) (Bys)
            (Bz)   (      0                          0         1 ) (Bzs)


      6) Data was transformed to geophysical coordinates: Data are transformed
         from inertial rotor coordinates to the Earth Mean Equatorial (equinox
         1950) coordinate system. This system is directly supported by the
         SPICE software provided by the Navigation and Ancillary Information
         Facility (NAIF) at JPL as inertial coordinate system 'FK4'. The
         angles required for this transformation come directly from the
         Galileo Attitude and Articulation Control System (AACS) data. The
         transformation matrix for this rotation is:


       --                                                                   --
       | (cosTsinDcosR - sinTsinR)  (-sinDsinTcosR - cosTsinR)      cosDcosR |
       |                                                                     |
       | (cosTsinDsinR + sinTcosR)  (-sinDsinTsinR + cosTcosR)      cosDsinR |
       |                                                                     |
       | -cosDcosT                  sinTcosD                        sinD     |
       --                                                                   --

         where

    R                              = Rotor-Right Ascension
    D                              = Rotor-Declination
    T                          = Rotor-Twist - Rotor-Spin-angle  (despun data)

         Once in an inertial coordinate system, SPICE software provides
         subroutines which allow a user to construct coordinate system
         transformation matrices for any ephemeris time. These matrices
         were constructed from the SPICE kernels by directly or indirectly
         extracting the primary and secondary vectors defining the
         coordinate system and then following the procedure outlined in
         the coordinate systems section of this document. The spacecraft/
         planet (SPK) , leap second (TS), and planetary constants (PCK)
         kernels required for these transformations have been archived in
         the PDS by NAIF. These SPICE kernels are available on the CD_ROM
         which contains the magnetometer data. The SPICE toolkit (software)
         can be obtained from the NAIF node of the PDS for many different
         platforms and operating systems. At the time of this archive, the
         SPICE toolkit was available via an anonymous-ftp site at
         naif.jpl.nasa.gov"



    CONFIDENCE_LEVEL_NOTE 

      Data Confidence Level:

      Data quality assessment is a rather vague concept which we
      will try to address in a somewhat qualitative manner. Each
      aspect of the data processing sequence can be analyzed to
      determine its maximum possible error contribution. In theory,
      these errors could be summed to provide estimates of the
      maximum error for each data point. We have not taken our
      error analysis to that level. We believe that our calibrations
      (sensor geometry and gains) are good enough that they produce
      a negligible source of data error. In addition, we believe that
      the coordinate system transformations which are derived from
      the SPICE kernels and Toolkit are negligible sources of error
      in the magnetic field vectors. The sources of error which we
      feel are the most significant are those associated with magnetic
      sources aboard the spacecraft, especially those with temporal or
      spacecraft orientation variations. The next greatest contributor
      of error is the data from the AACS which affects our knowledge
      of the spacecraft orientation and hence rotates the magnetic
      field vector. Lastly, telemetry or software errors which produce
      'spikes' or bit errors in the data are error sources.

      In regions where the magnetic sources associated with the
      spacecraft are fairly constant, magnetic interference is
      probably reduced by data processing to better than 0.01 nT
      at the inboard sensors. In these same regions, sensor zero
      levels (offsets) are known equally well. The data processing
      software does a fairly good job of removing all currently
      identified sources of magnetic interference.

      Our data processing software creates a data quality flag
      (dqf) which is an assessment of AACS and telemetry error
      source contamination of a given data point. This number
      is a binary integer where each bit indicates the presence
      or absence of some error source. The number 0 represents
      the absence of all error sources which are tested. The higher
      order bit (larger number) error sources are considered to be
      more significant error sources. Data are examined for
      gradients in the field which might be associated with telemetry
      bit errors, for regions of bad AACS angles, and for completely
      missing data. If the error is considered completely unrecoverable,
      the data values are replaced with a missing data flag. In the
      case of a flag in the rotor spin angle, the vector components
      may be flagged but the magnitude is still valid. Here is a list
      of all of the error checks and the bits they set in the dqf field.


      DQF_GOOD_DATA                 0   Good data
      DQF_BX_GRAD_WARNING         2^0   Component gradient warning
      DQF_BY_GRAD_WARNING         2^1   Component gradient warning
      DQF_BZ_GRAD_WARNING         2^2   Component gradient warning
      DQF_INTERP_ROTATTR          2^3   Missing rotor RA interpolated
      DQF_INTERP_ROTATTD          2^4   Missing rotor DEC interpolated
      DQF_INTERP_SPINDELT         2^5   Missing rotor Spin Delta interpolated
      DQF_INTERP_SCRELCON         2^6   Missing Relative Cone
                                          angle interpolated
      DQF_INTERP_SCRELCLK         2^7   Missing Relative Clock
                                          angle interpolated
      DQF_INTERP_ROTATTT          2^8   Missing rotor Twist interpolated
      DQF_INTERP_SPINANGL         2^9   Missing rotor Spin interpolated
      DQF_ROTATTR_FLAG            2^10  Missing rotor RA flagged
      DQF_ROTATTD_FLAG            2^11  Missing rotor DEC flagged
      DQF_SPINDELT_FLAG           2^12  Missing rotor Spin Delta flagged
      DQF_SCRELCON_FLAG           2^13  Missing Relative Cone angle flagged
      DQF_SCRELCLK_FLAG           2^14  Missing Relative Clock angle flagged
      DQF_ROTATTT_FLAG            2^15  Missing rotor Twist flagged
      DQF_AACS_TELEMETRY_HIT_FLAG 2^16  Telemetry hit in AACS record
      DQF_MAG_TELEMETRY_HIT_FLAG  2^17  Telemetry hit in mag record
      DQF_SPINANGL_FLAG           2^18  Missing rotor Spin flagged

      DQF_BX_GRAD_ERROR           2^25  Component gradient error
      DQF_BY_GRAD_ERROR           2^26  Component gradient error
      DQF_BZ_GRAD_ERROR           2^27  Component gradient error
      DQF_BX_FLAG                 2^28  Component flagged
      DQF_BY_FLAG                 2^29  Component flagged
      DQF_BZ_FLAG                 2^30  Component flagged


      Magnetic field gradient warning or error levels are set during
      the data processing according to expected variances depending on
      the region of space. In the solar wind, gradient warnings are
      usually issued at gradients of 10 nT/sec and errors at 15 nT/sec.
      AACS angles are interpolated across gaps during the processing
      if the gap length is relatively short (less than 10 minutes
      typically). If the gaps in spacecraft attitude are long, the AACS
      angles are flagged and not interpolated.

      Errors associated with AACS angles have various effects on the
      data. The rotor right ascension and declination are crucial to
      the understanding of the spacecraft orientation. Fortunately,
      these angles are slowly varying and can be interpolated to
      better than 1 degree of accuracy for long (many hour) time
      periods except near major spacecraft maneuvers. The relative
      clock and cone angles are used to remove scan platform
      interference. In their absence, no interference is removed
      (+/- 0.15 nT error possible in each component). The rotor motion
      spin delta is used to determine the instantaneous spin frequency
      for the phase delay computation. In its absence, the last known
      phase delay is applied to the current data point. The rotor spin
      angle and twist angle must be present in order to despin the data.
      These angles are generally not interpolated for more than ten
      minutes because the rotor spin period drifts over time periods on
      this order.