*****File RADWAV.DOC                                                          
                                                                              
                                                                              
                                                                              
                            I. BACKGROUND                                     
                                                                              
                                                                              
        On September 11, 1985, the International Cometary Explorer (ICE;      
 originally called ISEE-3) spacecraft made in situ measurements of            
 particles, fields and waves as it traversed the plasma tail of comet         
 Giacobini-Zinner (G-Z). The time of closest approach was approximately       
 11:02 UT and occurred at a tailward distance of 7,800 km. The spacecraft     
 was inside the bow wave for roughly 3 hours and in the main tail for about   
 10 min (Brandt et al., 1985;  Brandt et al., 1988, and references            
 therein).                                                                    
                                                                              
        Data from some of the instruments on the ICE spacecraft are           
 included on this CD-ROM archive for the period 08-14 September, 1985.        
 Ephemeris data giving hourly values of the ICE spacecraft trajectory         
 relative to Earth, Sun and G-Z are included in a separate file. Note         
 that the deviation of the spacecraft from uniform linear motion was          
 negligible during the encounter, so that interpolation of the trajectory     
 is straightforward.                                                          
                                                                              
                                                                              
 References:                                                                  
 ----------                                                                   
                                                                              
 Brandt, J.C., M.B. Niedner, and T. von Rosenvinge, "The ICE Project,"        
 Adv. Space Res., v.5, 3-16, 1985.                                            
                                                                              
 Brandt, J.C., "The International Cometary Explorer (ICE) Mission to          
 Comets Giacobini-Zinner and Halley" in "Space Missions to Halley's Comet",   
 p. 99-115, R. Reinhard, B. Battrick (Editors), ESA SP-1066, ESA              
 Publications Division, Noordwijk, The Netherlands, ISBN 0379 6566, 1986.     
                                                                              
 Brandt, J.C., R.W. Farquhar, S.P. Maran, M.B. Niedner, Jr., and T.T.         
 von Rosenvinge, "The International Cometary Explorer" in "Exploration        
 of Halley's Comet. Based on the 20th ESLAB Symposium, held in                
 Heidelberg, F.R.G., 27-31 October 1986," p. 969-980.                         
 M. Grewing, F. Praderie, R. Reinhard (Editors). Springer-Verlag,             
 Berlin, F.R.G. 23+984 pp. ISBN 3-540-17344-7 (F.R.G.), ISBN                  
 0-387-17344-7 (USA), 1988.                                                   
                                                                              
 Epstein, G., Hoang, S., Huntzinger, G., Steinberg J. -L., Fainberg, J.,      
 Grena, F., Mosier, S.R., and Stone, R.G.,  "The 3-Dimensional Radio Mapping  
 Experiment (SBH) on ISEE-C", IEEE Trans. on Geoscience Electronics, GE-16,   
 191, 1978.                                                                   
                                                                              
 =========================================================================    
                                                                              
                  II. Radio Mapping Experiment Derived Data                   
                                                                              
     This file describes the values of the density and temperature of         
the electrons measured (radio mapping) during the tail crossing of comet      
Giacobini-Zinner by ISEE-3/ICE as derived from spectroscopy of the            
thermal noise spectrum. The data was provided to the National Space           
Science Data Center (NASA/GSFC) by the Principal Investigator of the          
Radio Mapping Experiment on ISEE-3/ICE, Dr. Jean-Louis Steinberg of           
the Observatoire de Paris, Meudon, France. The instrument is described        
in "The 3-dimensional Radio Mapping Experiment (SBH) on ISEE-C", by R.        
Knoll, G.Epstein, S.Hoang, G.Huntzinger, J.L.Steinberg, J.Fainberg,           
F.Grena, S.R.Mosier, and R.G.Stone, IEEE Transactions on Geoscience           
Electronics, vol. GE-16, No. 3, pp.199-204, July 1978. The data cover         
the time interval from 10:00 UT to 12:00 UT on September 11, 1985. The        
time resolution is 54 seconds.                                                
                                                                              
	Since this method of measuring plasma parameters is relatively               
new, users of these data are referred to the following papers:                
                                                                              
    N.Meyer-Vernet, P.Couturier, S.Hoang, C.Perche, J.-L. Steinberg,          
    J.Fainberg and C.Meetre, Science, Vol.232, p.370, 1986.                   
                                                                              
    N.Meyer-Vernet and C.Perche, J. Geophys. Res., Vol.94, p.2405, 1989.      
                                                                              
	To derive the plasma parameters, it is assumed that the                      
electron distribution function can be approximated by a bi-maxwellian.        
The density given below is the total electron density (both electron          
populations) derived from the cut-off frequency of the thermal noise          
spectrum. The temperature is that of the cold electron population             
which is always the dominant one. Error bars on the two measured              
quantities are given in the first of the above mentioned papers.              
                                                                              
   TIME       N       T                                                       
  HHMMSS    cm-3     Deg. K                                                   
                                                                              
  100000    9.46  0.1585E+06                                                  
  100054    7.69  0.1585E+06                                                  
  100148    8.11  0.1585E+06