***** File SP2.DOC                                                            
                                                                              
                         TABLES                                               
                                                                              
OF DUST PARTICLE SPATIAL AND MASS DISTRIBUTIONS IN COMET P/HALLEY             
FROM SP-2 EXPERIMENT ON BOARD VEGA 1 AND VEGA 2 SPACECRAFT                    
                                                                              
                                                                              
1. THE SP-2 EXPERIMENT                                                        
                                                                              
The SP-2 experiment on Vega spacecraft was intended for studying              
the spatial and mass distributions of dust particles in the                   
cometary coma over the mass range 1. x 10**-16 to 1. x 10**-6 g. Covering     
such a broad mass range was made possible by using sensors of two             
types, namely, impact plasma and acoustic.                                    
                                                                              
Experiment tasks and measurement procedures                                   
                                                                              
    Dust particle velocities in the coma are small compared to the            
encounter velocity. In the cometary nucleus reference system the              
encounter pattern envisages the flyby module passage through the cloud        
of motionless dust particles, with the velocity V along the trajectory        
with the minimum distance from the nucleus, Ro.                               
                                                                              
    At every trajectory point with the distance R to the nucleus,             
where the density of dust particles with masses larger than some              
specified value m, is n(R) (> m), a surface with area S normal to the         
velocity vector V, is subjected to dN/dt(> m) = nR (> m) SV impacts with      
dust particles per unit time. Thus, by measuring this value for               
different R and m we can determine n(R) (> m), (the value we are              
interested in). This direct measurement method obviously makes it             
possible not only to determine the general dependence of dust particle        
densities on their distance to the nucleus, as well as their mass             
distribution, but also to detect variations of these characteristics,         
due to the non-stationary processes in the nucleus (explosion-induced         
shedding of outer layers, rotation and so on).                                
                                                                              
Instrument components                                                         
                                                                              
    The SP-2 system consists of impact detectors of two types,                
acoustic and ionization. A general view of the instrument with block          
diagram is given in 'Venus-Halley Mission' (Balekanov 1985). The basic        
acoustic detector is a thin circular membrane (500 cm**2 in area) with        
three piezoelectric elements. While a particle impacts the membrane           
the wave due to the flexural strain propagates. The force acting upon         
a piezoelectric element and proportional to the acceleration vertical         
component generates an electric signal. The acoustic detector is              
sensitive to the momentum imparted to the membrane during the                 
impact. The hyper-velocity impact of a dust particle is accompanied by        
a micro-explosion that results in forming the crater out of which a           
dense highly-ionized plasma is ejected. The value of recoil momentum          
associated with this ejection may be sufficiently higher than that of         
intrinsic momentum of the dust particle P = MV. The numeric                   
simulation of the impact yields the estimates showing that at 80 km/s         
the recoil momentum may be higher than the initial momentum P = MV by         
an order of magnitude. The accurate estimation of K-factor prevents a         
serious problem in calibrating such kind of detectors.                        
                                                                              
    The piezoelectric microphone output signal enters the                     
preamplifier. Because of the very short impact duration the                   
signal-power frequency spectrum extends to the high ultrasonic                
frequency region. A high-frequency signal component (about ~ 160 kHz)         
is amplified by the narrow-band amplifier and detected. At the output         
the signal dynamic range ~5x10**6 is divided into 16 channels with            
constant relative-variation of the threshold delta/m = 2.82 that allows       
measuring the particle mass spectrum n ( > m) at 16 equi-spaced points        
on the log m scale. Two detectors and two identical independent               
detecting circuits are used to make measurements more reliable. The           
third central piezoelement controls the in flight calibration. It             
regularly receives a calibrated electric pulse converted by the               
detector into the mechanical pulse to simulate the impact with a              
particle of certain mass.                                                     
                                                                              
    According to the preliminary estimates obtained from the                  
well-known Comet dust envelope models the counting rate of small dust         
particles may be very high. When a particle impacts the piezoelectric         
element, the latter is subjected not only to the forward wave caused          
by strain but also to the waves reflected from the membrane edges. Due        
to this effect the output signal is considerably delayed in time and          
thereby the impact counting rate will be limited to < 50 to 100 1/s.          
It means that the instrument's time resolution can prove insufficient         
and the saturation may be reached long before the closest approach to         
the Comet. To avoid this the wave reflections from the membrane edge          
are suppressed by the damper inserted along the membrane perimeters,          
which has an output signal of rather short duration (not more than 1          
ms) due to the efficient suppression of reflections.                          
                                                                              
    The acoustic detector is mounted on the instrument's body via             
three acoustic insulators to protect the detector against mechanical          
noises.                                                                       
                                                                              
    The dust particle ionization detectors are placed in four                 
cylinders served as the load-bearing structural elements. The                 
detectors are identical and arranged in pairs. The detectors of each          
pair are connected to two individual measuring systems to make                
measurements more reliable. A dust particle passes through the set of         
deflecting electrodes and grids which protect the detector inner pan          
from the exposure to the surrounding plasma and electromagnetic               
fields, and hits the lower electrode surface. The highly ionized dense        
plasma cloud is expanded in the lower chamber, then the charges of            
opposite sign are separated by the electric field and collected by the        
chamber electrodes to which the potential 2kV is applied.                     
                                                                              
    The instrument measures the total charge of electrons collected on        
the lower electrode.                                                          
                                                                              
    The published results of the laboratory studies of the hyper-             
velocity impact show that the charge Q ~ [m**(alpha)][V**(beta)] where        
alpha ~ 1, beta ~ 3. With the constant velocity of particles, as in           
our case, the total charge is proportional to their mass.                     
                                                                              
    The dynamic range of the ionization detectors is 10**5. It is             
divided into six output channels to measure a dust-particle mass              
spectrum at six points on the mass scale with a factor of an order of         
magnitude. The SP-2 instrument was not intended to realize the maximum        
possible sensitivity of the ionization technique. Smallest dust               
particles are measured with the VEGA SP-1 instrument.                         
                                                                              
    The regions of mass measurements with the acoustic and ionization         
detectors are overlapped appreciably that should allow comparing the          
data independently obtained on micron and submicron dust particles.           
Such a procedure may reduce uncertainty due to calibration errors and         
permit a more reliable comparison between the data about the particles        
which dominate the solar light scattering and the results of remote           
photometry and polarimetry of the Comet.                                      
                                                                              
SP-2 performance characteristics                                              
                                                                              
    The threshold sensitivity of the dust particle acoustic detector          
in terms of the transferred momentum is given by Pmin ~ 2x10**-5              
gcm/s.  Taking into account that the recoil momentum may exceed the           
particle momentum mV by 5 to 10 times, the minimum mass of recorded           
particles is < 3x10**-13 g.  The measurement range n (> m)x3x10**-13          
to ~ 2x10**-6 g is divided into 16 channels. With the relative width          
delta/m ~ 2.82, sensitive area S = 500 cm**2, accumulation time for one       
spectrum is 1 s, which corresponds to the spatial resolution ~ 80 km          
over the flyby trajectory. The counting rate of small mass particles          
is about 4095 1/s.                                                            
                                                                              
    The ionization detector is capable of recording particles with            
mass 3x10**-16 to 3x10**-11g. The number of channels is 6, with               
relative width delta/m = 10, sensitive area - 40 cm**2. The limit             
counting rate of small mass particles is ~ 65,500 1/s. The                    
accumulation time for one spectrum is 1 s.                                    
                                                                              
    As it was mentioned above, the detector and measuring systems of          
the instrument are backed-up. The instrument represents the results of        
measurements and flight tests for each cycle in a digital format of           
200 bit. It may dump the data to either high-speed or low-speed link          
or to both simultaneously at a rate 65,535 bit/s and 3072 bit/s,              
respectively.                                                                 
                                                                              
    The instrument mass is 4 kg, power consumption, 3.5 W.                    
                                                                              
    The test support equipment is used to test the instrument                 
functioning in all modes.                                                     
                                                                              
    The instrument was developed by the Soviet specialists.                   
                                                                              
Balebanov, V.M., Skuridin, G.A., Vorontsova, E.V., Bassolo, V.S.(eds.):       
1985, Venus-Halley Mission, Louis-Jean, Gap                                   
                                                                              
Mazets, E.P., Aptekar, R.L., Golenetskii, S.V., Guryan, Y.A.,                 
Dyachkov, A.V., Ilyinskii, V.N., Panov, V.N., Petrov, G.G.,                   
Savvin, A.V., Sagdeev, R.Z., Sokolov, I.A., Khavenson, N.G.,                  
Shapiro, V.D., Shevchenko, V.I., 1986, Nature 321, 276                        
                                                                              
Mazets, E.P., Sagdeev, R.Z., Aptekar, R.L., Golenetskii, S.V.,                
Guryan, Y.A., Dyachkov, A.V., Ilyinskii, V.N., Panov, V.N.,                   
Petrov, G.G., Savvin, A.V., Sokolov, I.A., Frederiks, D.D.,                   
Khavenson, N.G., Shapiro, V.D., Shevchenko, V.I.,                             
1987, Astron. Astrophys. 187, 699-704                                         
                                                                              
                                                                              
2. OBSERVATIONS AND DESCRIPTION OF THE DATA TABLES                            
                                                                              
The flyby trajectories of the Vega spacecraft in the cometocentric            
frame can be specified by the coordinates of the closest approach             
to the nucleus R0(R0x,R0y,R0z) and the components of the relative             
velocity V(Vx,Vy,Vz). The corresponding values for Vega1 and Vega2            
were as follows:                                                              
                                                                              
Vega 1:   R0x = 7830 km;      R0y = 2480 km;      R0z = 3400 km;              
          Vx = 28.64 km/s;    Vy = -72.73 km/s;   Vz =-12.95km/s;             
                                                                              
Vega 2:   R0x = 7100 km;      R0y = 2680 km;      R0z = 2630 km;              
          Vx = 30.53 km/s;    Vy = -69.44 km/s;   Vz =-11.88km/s;             
                                                                              
If the results of the dust flux measurements are referred to the              
time reckoned from the instant of closest approach, the                       
corresponding distances to the cometary nucleus can be found as               
R=R0*sqrt(1 + (t/t0)**2), where the parameter t0 = R0/V. In the               
course of measurements the numbers of particle impacts with masses            
exceeding the channel threshold is counted in each pulse height               
channel at 1 second intervals along the trajectory:                           
                                                                              
               N(>m) = F(>m)*S*T = n(>m)*V*S*T,                               
where n(>m) is the number density, F(>m)=n(>m)*V the cumulative               
flux, S the effective sensor area (500 cm2 for the acoustic sensor            
and 28.57 cm2 for the impact plasma one), T=63/64s the accumulation           
time in each measurement.                                                     
                                                                              
For the acoustic sensors, dead time corrections were introduced at            
channel count rate N(>m) > 50/s. For the fast impact plasma sensors           
such corrections were not needed.                                             
                                                                              
The SP-2 data for Vega1 spacecraft are formatted into table containing        
2092 records. Each record consists of 18 columns and contains time of         
measurement referred to "closest approach" (where 0 sec is 4:12:38 UT         
adopted from SP-1 experiment), 5 columns of impact plasma sensor data,        
and 12 columns of acoustic sensor data.                                       
                                                                              
The data table for Vega2 is similar but record contains 14 columns for        
acoustic sensor data, total 20 columns. Total number of records is 2267.      
                                                                              
Below are the mass threshold values (in gramms) for the table columns         
described.                                                                    
                                                                              
                                                                              
Column    Data        Vega1             Vega2                                 
          type                                                                
  1        ---        time              time                                  
                                                                              
  2       Plasma    N( > 6.e-16 )     N( > 6.e-16 )                           
  3       Plasma    N( > 6.e-15 )     N( > 6.e-15 )                           
  4       Plasma    N( > 6.e-14 )     N( > 6.e-14 )                           
  5       Plasma    N( > 6.e-13 )     N( > 6.e-13 )                           
  6       Plasma    N( > 6.e-12 )     N( > 6.e-12 )                           
                                                                              
  7       Acoustic  N( > 1.5e-11 )    N( > 6.6e-13 )                          
  8       Acoustic  N( > 4.1e-11 )    N( > 1.8e-12 )                          
  9       Acoustic  N( > 1.2e-10 )    N( > 5.2e-12 )                          
  10      Acoustic  N( > 3.3e-10 )    N( > 1.5e-11 )                          
  11      Acoustic  N( > 9.2e-10 )    N( > 4.1e-11 )                          
  12      Acoustic  N( > 2.6e-9 )     N( > 1.2e-10 )                          
  13      Acoustic  N( > 7.3e-9 )     N( > 3.3e-10 )                          
  14      Acoustic  N( > 2.1e-8 )     N( > 9.2e-10 )                          
  15      Acoustic  N( > 5.8e-8 )     N( > 2.6e-9 )                           
  16      Acoustic  N( > 1.7e-7 )     N( > 7.3e-9 )                           
  17      Acoustic  N( > 4.7e-7 )     N( > 2.1e-8 )                           
  18      Acoustic  N( > 1.3e-6 )     N( > 5.8e-8 )                           
  19      Acoustic  -----             N( > 1.7e-7 )                           
  20      Acoustic  -----             N( > 4.7e-7 )